Time protocols
Time protocols
Protocol	DC bal.	PLL	Medium	Transmit	Receive	Encoding	Record	Rate	WRT- CLK	Future
White rabbit	Y	Y	RX+TX (Fiber)	Spec. HW	Spec. HW	Ethernet, / 8b10b		1.25 GHz		“Gold standard”, / Reference
Ratatime	Y		Any*	FPGA	FPGA	Self-align pattern		1 – 10 MHz	Out	Deprecate
Heimtime			Any*	FPGA	PC (complex)	Periodic + data	Y	200 – 400 Hz, varying	Out	Deprecate
Rataclock PLL	Y	Y	Any*	FPGA	FPGA	Clock w. PWM data		> 5 MHz	Out
Rataclock slow	Y	(Y)	Any*	FPGA / WR-LM32	FPGA	Clock w. PWM data		1 – 10 MHz	Out
Heimtime II			Any*	WR-LM32 / FPGA	PC / FPGA	Periodic + data	Y	10 Hz – 100 kHz		FPGA versions
Clock + / “Schakel”	Y + N	Y	2x LVDS	FPGA	FPGA	Clock / / Time data		Clock: 200 MHz / 50 MHz @ 100 kHz	In
Clock + / reset	Y + N	Y	2x Any*	(FPGA)	(FPGA)	Clock / Reset				DO NOT USE !
Clock +
HT II
Silent drift
Own time
Not really a timing protocol.
Mentioned for completeness.
“Androm till skräck or varnagel.”
DC balanced:	Fixed long-term average of 0 and 1 signal.
PLL:	PLL clock recovery.
1-wire:	Protocol uses one signal. (Any medium.)
Transmit:	Code for transmitter.
WR-LM32 is softcore in WR modules.
Receive:	Code for receiver.
Record:	Suitable for DAQ recording. (Low rate.)
Rate:	Approximate signal rate / bandwidth.
WRTCLK:	Handled by WRTCLK Exploder gateware.
For good
continuous
monitoring:
FPGA decoder
Suitable for DAQ
recording
White text:
Dev/future
* Any = NIM, ECL, LVDS, … Fiber for DC-balanced.

---
Foot-prints
Foot-prints in the scope
Protocol	DC bal.	PLL	Medium	Encoding	Rate	Future
White rabbit	Y	Y	RX+TX (Fiber)	Ethernet, / 8b10b	1.25 GHz	“Gold standard”, / Reference
Ratatime	Y		Any*	Self-align pattern	1 – 10 MHz	Deprecate
Heimtime			Any*	Periodic + data	200 – 400 Hz, varying	Deprecate
Rataclock PLL	Y	Y	Any*	Clock w. PWM data	> 5 MHz
Rataclock slow	Y	(Y)	Any*	Clock w. PWM data	1 – 10 MHz
Heimtime II			Any*	Periodic + data	10 Hz – 100 kHz	FPGA versions
Clock + / “Schakel”	Y + N	Y	2x LVDS	Clock / / Time data	Clock: 200 MHz / 50 MHz @ 100 kHz
Clock + / reset	Y + N	Y	2x Any*	Clock / Reset		DO NOT USE !

---
Clock and time distribution
Clock and time distribution
Readout:
8-10 μs ?
Dev. / Future
PEXARIA
Readout:
< 2 μs ?
TLU
TRLO II
TLU
LM32
WR
(Spartan6)
EXPLODER
Readout:
2 μs ?
VETAR
WRTCLK
Ratatime
SIS3316
TLU
WR
Rataclock (PLL)
200 MHz +
“Schakel”
Rataclock (slow)
FOOT
LM32
Heimtime
TRB (RPC)
T5ns
ALPIDE(?)
AIDA
Or replace with
Heimtime II
(Arria)
WR-EXPLODER
WR
LYCCA
Various
'uncooperative'
DAQs
TLU
LM32
Heimtime II
Uncooperative =
free-running,
but not prepared
for timestamping
→ Need to record time,
sort out in software...
(Bad monitoring.)
Rataclock (slow)
WR receivers:
Different form factors.
(Almost) same capabilities.
TAMEX, VFTX
coarse counter
sync
T5ns
Random pulses
at same time
at different places.
“PRNG”
(time based)
WR network